## Slide 1: iot.schema.org
Feature of Interest
Haystack Vocabulary Alignment
May 17, 2018

## Slide 2: Feature of Interest
Update on the meta-model

## Slide 3: Motivation for Feature Of Interest Pattern
Binds Capability and Interaction Patterns to real-world objects
This provides information about the environment in which sensing/actuating is applied
PlugFest use cases prove that the Feature of Interest (FoI) pattern is needed in iot.schema.org

## Slide 4: Feature Of Interest Pattern

## Slide 5: Feature of Interest Example
{
"@id": "iot:TemperatureSensing",
"rdfs:subClassOf": { "@id": "iot:Capability" },
"iot:providesInteractionPattern": [ { "@id": "iot:Temperature“ }]
}, {
"@id": "iot:Temperature",
"rdfs:subClassOf": { "@id": "iot:Property" },
"iot:isPropertyOf": {"@type": "iot:Room"},
"iot:providesOutputData": { "@id": "iot:TemperatureData“ }
}, {
"@id": "iot:TemperatureData",
"rdfs:subClassOf": { "@id": "iot:DataSchema" },
"iot:hasFeatureOfInterest": {"@type": "iot:Room"},
"iot:observedProperty": "iot:Temperature",
"schema:propertyType": { "@id": "schema:Float" },
"schema:unitCode": { "@id": "iot:TemperatureUnit" },
"schema:minValue": "schema:Float",
"schema:maxValue": "schema:Float"
}

## Slide 6: Haystack vocabulary in iot.schema.org
Extension of iot.schema.org

## Slide 7: Project Haystack
Aims to standardize semantic data models to unlock the value of data generated by building equipment.
It is an open source initiative to enable Internet of Things applications.
Applications include automation, control, energy, HVAC, lighting, and other environmental systems.

## Slide 8: Haystack Model
entity: is an abstraction for some physical object in the real world, e.g.
sites, equipment, sensor points, etc.
tag: is a name/value pair applied to an entity.
equip: is a physical asset, e.g. AHU, boiler, or chiller. Can also be used
to model a logical grouping, e.g. chiller plant.
point: is typically a digital or analog sensor or actuator
  sensor: input, AI/BI, sensor
  cmd: output, AO/BO, actuator, command
  sp: setpoint, internal control variable, schedule
kind: Defines a tag value type, e.g., number, bool, str
Multiple tags are used to model the role of a point:
  where: discharge, return, exhaust, outside
  what: air, water, steam
  measurement: temp, humidity, flow, pressure

## Slide 9: Integration of Haystack vocabulary in iot.schema.org

## Slide 10: Example: Boiler in Haystack
equip: boiler
It is used to generate hot water or steam for heating.
Equip level tags:
  where: equipRef must reference parent plant if associated with a plant
  what: hot water or steam or oil or gas
Points associated with the boiler equip:
  run cmd
  run sensor
  circ pump cmd
  circ pump sensor
  condensate pump cmd
  condensate pump sensor

## Slide 11: Example: Boiler mapped to iot.schema.org
iot:Capability: iot:Boiler
  subclasses: iot:HotWaterBoiler, iot:SteamBoiler, iot:OilBoiler etc
iot:InteractionPattern:
  iot:Action: iot:TurnOn, iot:TurnOff (run cmd)
  iot:Property: iot:RunStatus (run sensor)
  iot:Action: iot:CirculatePumpOn, iot:CirculatePumpOff (circ pump cmd)
  iot:Property: iot:CirculatePumpStatus (circ pump sensor)
  iot:Action: iot:CondensatePumpOn, iot:CondensatePumpOff (condensate pump cmd)
  iot:Property: iot:CondensatePumpStatus (condensate pump sensor)
What should be the result of mapping the Haystack vocabulary into iot.schema.org?

## Slide 12: Thank You!
Questions please…